## Slide 1: Micro D to Header Adapter Board Build
Lafe Spietz
NIST
2024
MEMSDuino

## Slide 2
MEMSDuino
Abstract
This circuit board breaks out the MicroD found at the base of many dilution refrigerators into a set of up to 20 lines, each broken out in a pair of identical 4 pin header outputs. Labels are specific to our switch matrix at NIST, but can be adapted to any switch with 20 or fewer lines.

## Slide 3: Parts
https://www.digikey.com/en/products/detail/itt-cannon,-llc/M83513%2F25-D01CP/4803943
https://www.amazon.com/Header-Lystaii-Pin-Connector-Electronic/dp/B06ZZN8L9S/
0.1” headers, 40 pin strips x1
M83513/25-D01CP x1
MEMSDuino

## Slide 4
66 x 44 mm size
Black solder mask
White silkscreen
1.6mm FR4
https://github.com/lafefspietz/MEMSduino/raw/main/PCB_files/microd-header-adapter-board-rev2-gerbers.zip
MEMSDuino

## Slide 5: Header breakaways: 4 pin x8
MEMSDuino

## Slide 6: Cut off the screws with a cutting wheel:
MEMSDuino

## Slide 7
MEMSDuino

## Slide 8: Mechanical Drawing
MEMSDuino

## Slide 9: Altium Designer Files
https://github.com/lafefspietz/MEMSduino/raw/main/PCB_files/microd-header-adapter-board-rev2.PcbDoc
https://github.com/lafefspietz/MEMSduino/raw/main/PCB_files/microd-header-adapter-board-rev2.SchDoc
https://github.com/lafefspietz/MEMSduino/raw/main/PCB_files/microd-header-adapter-board-rev2.PrjPcb
MEMSDuino

## Slide 10
MEMSDuino
Conclusions:
Note that pins 13 and 12 connect to ground. This might not be ideal in certain circumstances. We have broken ground at room temperature and use the metal in the dilution refrigerator for the ground now. This board will almost certainly be different from what other users will want. This example drives all 4 control lines of 4 MEMS switches.