## Slide 1: Control Panel Circuit Board
Lafe Spietz
NIST
2024
MEMSDuino

## Slide 2
MEMSDuino
Abstract
This is the control panel, where a human operator pushes buttons to set the state of the switch and can see indicator lights which display the state of the switch. Indicator lights are programmable RGB LED’s and buttons connect an analog pin on the Arduino to a resistor ladder.

## Slide 3: Order Circuit Boards
https://github.com/lafefspietz/MEMSduino/raw/main/PCB_files/9button-9neopixel-gerbers.zip
https://www.pcbway.com/
9button-9neopixel
MEMSDuino
228.6 x88.9 mm size
Black solder mask
White silkscreen
1.6mm FR4

## Slide 4: Order Components
https://www.amazon.com/ZYAMY-Dupont-Connector-Multicolor-Breadboard/dp/B0789F523N/
https://www.digikey.com/en/products/detail/yageo/MFR-25FBF52-10K/13219
https://www.adafruit.com/product/1559
https://www.digikey.com/en/products/detail/e-switch/TL59NF160Q/390533
4 Wire Header cable, 6” long x1
NeoPixel RGB programmable LED x9
10 kOhm axial resistor x9
Button x9
MEMSDuino

## Slide 5
MEMSDuino
Assembly

## Slide 6: Backside Detail of cable connection
MEMSDuino

## Slide 7: Dimensioned Drawing
MEMSDuino

## Slide 8
Button Ladder Schematic
Buttons connect analog line A4 on the Arduino to different nodes in a ladder of resistors which spans from 5 volts to a node just above ground. The analog line has a 100k pull down resistor on the Arduino Shield Circuit Board.
MEMSDuino

## Slide 9
PCB Layout
Created in Altium Designer
MEMSDuino

## Slide 10
MEMSDuino
Conclusions:
This board should get either replaced by or integrated into panels like the ones from frontpanelexpress.com for a more professional finish. These are cheaper and easier to rapid prototype, however.