## Slide 1: SP6T Control System
Lafe Spietz
NIST
2024
MEMSDuino

## Slide 2
MEMSDuino
Abstract
This system uses the MEMSDuino to control the SP6T switches available from CryoElec.

## Slide 3: Bill of materials
Wood Board
Custom metal box
Brass screws to fasten box to board
Steel screws to hold electronics down
3d printed standoffs and thread inserts
M-M short Jumpers
F-M long jumpers
SP6T switch from CryoElec
DB 25 socket connector
4-40 hex standoffs
MicroD to dual nanoD breakout board and bracket

## Slide 4: 4”x24”x0.5” White Oak Boards
https://ocoochhardwoods.com/detail/?i=124wo

## Slide 6: Print out template at 1:1 scale to trace hole locations to wood board

## Slide 7: Drill bits to use
1/16” bit: pilot holes and holes for wood screws.
1/8” bit: through holes for 4-40 screws
7/32” for 10-32 thumb screw clearance holes
5/32” to mill out slot for 4 wire header cable

## Slide 8: Knurled Brass Thumb Screws to Mount in Panel
https://www.mcmaster.com/92421A645/

## Slide 10
https://www.digikey.com/en/products/detail/norcomp-inc/171-025-203L001/858144
X1

## Slide 11
https://www.mcmaster.com/91075A462/
X2

## Slide 12
https://www.mcmaster.com/93465A113/
X4

## Slide 13
X7
https://www.mcmaster.com/90272A106/

## Slide 14
X2
front-panel-edge-bracket.STL

## Slide 15
X7
https://www.3djake.com/ruthex/threaded-insert-4-40-unc-100-pieces

## Slide 17
X6
https://www.mcmaster.com/98685A540/

## Slide 18
https://www.adafruit.com/product/1957
https://www.adafruit.com/product/1952

## Slide 19
https://www.cryoelec.com/products/cryoswitchsp6t

## Slide 22: Order Components
https://www.amazon.com/ZYAMY-Dupont-Connector-Multicolor-Breadboard/dp/B0789F523N/
https://www.digikey.com/en/products/detail/yageo/MFR-25FBF52-10K/13219
https://www.adafruit.com/product/1559
https://www.digikey.com/en/products/detail/e-switch/TL59NF160Q/390533
4 Wire Header cable, 6” long x1
NeoPixel RGB programmable LED x6
10 kOhm axial resistor x6
Button x6
MEMSDuino

## Slide 23
152.4 mm x 88.9 mm
Black solder mask, white silkscreen
MEMSduino\PCB_files\6button-6neopixel-gerbers.zip

## Slide 24
MEMSduino\PCB_files\6button-6neopixel-gerbers.zip

## Slide 25
Everything default but what is marked with red arrows
Pcbway.com

## Slide 26
Bud AN-1304-A Diecast Aluminum Box
https://www.mouser.com/ProductDetail/Bud-Industries/AN-1304-A?qs=9qK3lZr%252Bi0J%2FETgT9O2KyQ%3D%3D

## Slide 27
Bud AN-1304-A Diecast Aluminum Box
https://www.mouser.com/ProductDetail/Bud-Industries/AN-1304-A?qs=9qK3lZr%252Bi0J%2FETgT9O2KyQ%3D%3D

## Slide 28
X4
Use ¾” 4-40 screws to attach the main box to the wood board, with washers for each screw:
Be sure to orient box so that hole for cables points towards Arduino.

## Slide 29
Modify or buy already-modified AN-1304-A box as follows:

## Slide 30
Modify or buy already-modified AN-1304-A lid as follows:

## Slide 31
MEMSDuino

## Slide 32
MEMSDuino
Conclusions: