## Slide 1: Bud Box
MEMSDuino
Lafe Spietz
NIST
Summer 2024

## Slide 2: Tools and parts
Bud Industries AN-1304-A diecast aluminum box: $12.93
Assmann A-DF 25 PP/Z DB25 board mount connector: $1.17
McMaster Carr 91075A462 4-40 standoffs: 2x$3.73 = $7.46
4-40 tap
#43 drill bit for 4-40 tapped holes
1/8” mill tool
3/8” mill tool
Center drill
1/8” drill bit
(none of these machine tools are needed if you outsource the machining)

## Slide 3: AN-1304-A Diecast Aluminum Enclosure from Bud Industries
https://www.onlinecomponents.com/en/productdetail/bud-industries/an1304a-48608718.html

## Slide 6: Dsub Lid Assembly
https://www.digikey.com/en/products/detail/assmann-wsw-components/A-DF-25-PP-Z/1241794
https://www.mcmaster.com/91075A462/
Use pliers to tighten standoffs

## Slide 7: Adding polyimide tape to the lid
Prevent potential shorts
This must be assembled before the circuit board is soldered to the DB25 connector!

## Slide 8: Board mount/panel mount DB25
Cutout is 10.72 mm x 41.10 mm
No. 43